## Slide 1: Unit 4. Coding and Capacity on Fading Channels
Ece-gy 6023. Wireless communications
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Describe symbol mapping for QAM constellations
Implement symbol detection for faded symbols
  Compute average BER and SER on AWGN and flat channels and compare
Identify if a system can be modeled as slow vs. fast and frequency-selective vs. flat fading
For slow and flat fading, compute outage probability and capacity under a fading model
For IID fading, compute the ergodic capacity
Create a TX and RX chain for flat and fading channels with given components
  Symbol equalization, soft symbol detection, interleaving, channel decoder
Use MATLAB tools for common channel encoders and decoders
  Convolutional, turbo codes and LDPC codes

## Slide 3: Outline
Uncoded Modulation over Fading Channels
Capacity with Coding over Fading Channels: Outage Capacity
Capacity with Coding over Fading Channels: Ergodic Capacity
Review: Coding over an AWGN Channel
Coding over Fading Channels
Capacity with Bit-Interleaved Coded Modulation

## Slide 4: Uncoded Modulation
Symbol mapping
TX bits
TX filter
Fading channel
Symbol demodulation
RX filter
This section: Uncoded modulation over fading channels
  That is, communication with no channel encoding and decoding
We will show uncoded modulation works very poorly
Virtually all practical wireless systems use coding of some form
QAM symbols
RX QAM symbols
RX bits

## Slide 5: Mathematical Model
Symbol mapping
TX bits
Fading channel
Symbol demodulation
Simple memoryless model:
  and TX and RX QAM symbols
  : Fading channel gain, Noise
Assumptions:
  Perfect synchronization
  No ISI in the channel (or the equalizer has removed the effect of the ISI, more on this later)
  We can look at one symbol at a time
RX QAM symbols
RX bits
TX QAM symbols

## Slide 6: Review: Bit to Symbol Mapping
= sequence of bits.
= sequence of complex symbols
  Each symbol has one of possible values
Modulation rate: bits per symbol
  Each bits gets mapped to one symbol
Symbol period: One symbol every seconds.
Bit rate of bits per second
T
Ex. with M=4 symbols =2 bits per symbol

## Slide 7: Review: QAM Modulation
QAM: Most common bit to symbol mapping in wireless system
  bits mapped to and bits mapped to Q
  Each dimension is mapped uniformly
bits/sym
bits/sym
bits/sym
QPSK

## Slide 8: ML Estimation for Symbol Demodulation
Consider single symbol:
  Drop the sample index
  is a QAM symbol
Maximum likelihood estimation:
Given and :
Hence,

## Slide 9: Equalization and Nearest Symbol Detection
Likelihood:
MLE is:
Here, = equalized symbol.
Procedure:
  Step 1: Equalize the symbol:
  Step 2: Find closest to in the complex plane

## Slide 10: Decision Regions
ML estimate is closest point in constellation to :
Decision region for a point :
  set of points where is the closest point:
Decision region for s1
s1 (closest point)
s2
s3
s4
Example: Decision region in QPSK

## Slide 11: Error Probabilities on an AWGN Channel
Error probabilities:
  Symbol error rate, SER: Prob symbol is misdetected
  Bit error rate, BER: Probability of a bit is in error
  Assume TX symbols are uniformly distributed
First consider AWGN model:
  No fading
SER for QPSK can be shown to be:
  SNR =
z
w
No error
z in correct decision region
Error
z not in correct decision region
sm
sm
w
z

## Slide 12: SER for AWGN Modulation
Error formula can be derived for most QAM mappings
  See, e.g., Proakis
For an AWGN channel:
  SER typically decays exponentially with SNR
  Ex: for QPSK

## Slide 13: Ex: BER Simulation for 16-QAM
See demo
Easy to do in MATLAB

## Slide 14: SNR on a Fading Channel
Now return to a fading channel:
Equalization:
  Effective noise after equalization
SNR after equalization:
  Noise energy after equalization:
  SNR is
  SNR varies with the fading
Average SNR is:
High SNR
Low SNR
SNR:

## Slide 15: Average SER on a Fading Channel
Fading channel:
With fading, SNR is random ,. SNR is
Define the average SER:
  A function of the average SER
  Represents the average over independent channel realizations
If is Rayleigh distributed, is exponential with

## Slide 16: Example: SER on QPSK with Rayleigh Fading
Rayleigh fading: is exponential
QPSK: for large
Lemma: Suppose that is exponential
  Detailed proof below. Write
Average SER: From Lemma
Average SER decays as
In AWGN channel, SER decays as
Much slower decay

## Slide 17: Comparison of Fading vs. AWGN
Error rate with fading is dramatically higher.
Ex. for QPSK:
  No fading, SER decays exponentially
  With fading, SER decays with inverse SNR
Similar relations for most other constellations
Need much higher SNR
SER with QPSK
No fading
Rayleigh fading

## Slide 18: 16-QAM Example
See demo
Large gap between AWGN and Rayleigh

## Slide 19: Lemma for Average of Q function
Lemma: Suppose that is exponential .
Proof:
  Change order of integral

## Slide 20: In-Class Exercise

## Slide 21: Outline
Uncoded Modulation over Fading Channels
Capacity with Coding over Fading Channels: Outage Capacity
Capacity with Coding over Fading Channels: Ergodic Capacity
Review: Coding over an AWGN Channel
Coding over Fading Channels
Capacity with Bit-Interleaved Coded Modulation

## Slide 22: Coding Over Fading Channels
Lesson from previous section:
  With fading, uncoded modulation cannot provided sufficient reliability
  Error rate decays slowly with SNR
Channel coding:
  Send data in blocks
  Block contains redundancy
  If some parts fade, can still recover block
All commercial wireless systems use coding!

## Slide 23: Time and Frequency Fading
Recall: Channels vary over time and frequency
Variation in time:
  Due to Doppler spread,
  Coherence time,
  Time over which channel changes significantly
Variation in frequency
  Due to delay spread
  Coherence bandwidth,
  Frequency over which channel changes significantly
MHz
ms
20 path random channel with Hz, ns
SNR [dB]

## Slide 24: Flat vs. Frequency-Selective Fading
Suppose we transmit a coding block
  and in bandwidth
  region in time and frequency
Flat fading:
  Channel does not vary in frequency over coding block
Frequency selective fading:
  Channel varies over frequency
Frequency selective
Flat

## Slide 25: Slow vs. Fast Fading
Suppose we transmit a coding block
  and in bandwidth
  region in time and frequency
Slow fading:
  Channel does not vary in time over coding block
Fast fading:
  Channel varies over frequency
Fast
Slow

## Slide 26: Summary: Four Regimes
Transmission time
Transmission bandwidth
Fast, Frequency selective
Slow, Frequency selective
Slow, Flat
Fast, Flat
Coding block

## Slide 27: Regimes to Model Coding
Transmission time
Transmission bandwidth
Fast, Frequency selective
Slow, Frequency selective
Slow, Flat
Fast, Flat
To analyze fading, consider two extreme cases
Flat and slow fading over coding block:
  Channel is flat and slow fading over coding block
  All symbols see approximately same fading
IID fading in coding block:
  Channel fades in time and/or frequency over block
  Fast and/or frequency selective
  Model as large number of independent fades

## Slide 28: Analysis of Coding with Flat and Slow Fading
Coding block sees an SNR
SNR varies but is constant over each block
  Transmission time Coherence time
  Transmission bandwidth Coherence bandwidth
Suppose code has some target SNR
  Target could be based on some block error probability
Assume has some distribution
Outage probability:
  The fraction of time target is not met
  Can be computed from the distribution of
Coding block

## Slide 29: Outage Probability for Rayleigh Fading
Suppose a channel is Rayleigh fading
SNR is exponentially distributed with some mean
Outage probability:
Average SNR for a given outage probability:
Fade margin: Additional SNR needed above target for a given outage probability:
  In linear scale:
  In dB:

## Slide 30: Fade Margin Example
Example:
  Target SNR is dB
  Outage probability:
From previous slide, necessary average SNR is: dB
The average SNR needs to be 20 dB above target!
Plot: Fade margin vs. outage
Fade margins with Rayleigh fading can be enormous!
Max fade
20 dB fade margin
Fade=0

## Slide 31: Outage Capacity
Suppose we can achieve some rate as a function of SNR
When SNR is random, so is the rate
Outage capacity: Rate, we can achieve with a probability
Example:
  Suppose system has 20 MHz bandwidth and the rate is 60% of Shannon capacity
  The average SNR is 20 dB.
  What is the outage capacity for 1% outage assuming Rayleigh fading?
Solution:
  From earlier, for Rayleigh fading, the SNR achievable at the outage probability is
  In linear scale,
  Outage capacity: Mbps
  At the average SNR the rate is Mbps

## Slide 32: System Implications for Outage
With flat and slow Rayleigh fading, need to add large fade margin
Channel coding does not mitigate fading
  Fading causes all bits to fail
  Still may be useful to use channel coding (e.g., for noise across the symbols)
Possible solutions?
  If there is motion, perhaps we can retransmit later
  Go to a lower rate (needs less SNR)
  Just accept that some locations are in outage
Some of these solutions are discussed in the next unit

## Slide 33: Outline
Uncoded Modulation over Fading Channels
Capacity with Coding over Fading Channels: Outage Capacity
Capacity with Coding over Fading Channels: Ergodic Capacity
Review: Coding over an AWGN Channel
Coding over Fading Channels
Capacity with Bit-Interleaved Coded Modulation

## Slide 34: IID Fading Model
Coding block with fast and/or frequency selective fading
Simple mathematical model:
  Each is a symbol in time and frequency
  Assume channel gains are i.i.d. with some distribution
  and
  Each symbol experiences an SNR
  Number of symbols
Assumption implicitly assumes:
  We have a very large coding blocks in time or frequency
  Can experience many independent fades
Coding blocks with fast and/or frequency selective fading

## Slide 35: Ergodic Capacity
IID fading model:
  Channel gains are i.i.d. with some distribution
Ergodic capacity: Theoretical maximum rate per symbol
  Assume average transmit power limit
  Maximum taken over all codes and blocklength
  No computational limits
Theorem: Ergodic capacity of an IID fading channel is:
  Value is in bits per symbol
  Expectation is over channel distribution

## Slide 36: Shannon Ergodic Capacity Key Remarks
From previous slide, ergodic capacity is:
Theoretical result: Needs infinite computation and delay
  We will look at performance of real codes next
TX does not need to know channel
  But RX must estimate and use this channel.
  We will see RX design is critical
If TX knew the channel, it could get theoretically get slightly higher rate
  Uses a method called water-filling
  Place more power on symbols with better SNR.
  Gain is not typically large and rarely used in practical wireless systems

## Slide 37: Comparing Ergodic and Flat Capacity
Fading capacity is always lower than flat fading
  Keeping the same average SNR the same
  This fact follows from Jensen’s inequality:
But gap is not that large at low to moderate SNRs
  See graph to the right. Loss of only 1-2 dB in
Conclusions:
  We should try to code over large number of fading realizations
  In this case, the capacity loss is theoretically small
  Much better than the case of uncoded modulation
We will look at practical codes next

## Slide 38: Small-Scale and Large-Scale Fading
Up to now we have considered variations due to small scale fading
  Variations from constructive or destructive interference of multipath components
  May or may not cause variations within a coding block
  Ex: Variations within a few wavelength in one location in the office area
Most scenarios also have variations due to large scale fading:
  Changes in distance-based path loss, shadowing, angles, …
  Typically occur at slower time scales (100s of ms or more)
  Rarely causes variation over a coding block (typically 10s of ms or less)
  Ex: Moving within the office space to the right
Small scale region
Large scale region

## Slide 39: Analysis with Small- and Large-Scale Fading
Suppose SNR varies as :
  Vector of large-scale parameters, e.g., distance, angles, shadowing, etc.
  Small-scale parameters, e.g., time-frequency location of a degree of freedom
If fading in each coding block is slow and flat:
  Each coding block has an SNR
  Can compute outage probability:
  Probabilities computed over small-scale and large-scale parameters
If fading in coding block can be modeled as large number of i.i.d. samples of :
  Ergodic capacity is
  Take average over small-scale, but NOT large scale
  Rate is a function of
  Then outage probability is:

## Slide 40: Example: Rate CDF Calculation
Large-scale model:
  SNR due to large scale variations [Simple model just for exercise]
  = 10 dB and 100 m
  Distances vary uniformly in [50,200]m
Small scale model:
  Variation within a location is Rayleigh
  SNR at a particular time-freq DoF will be
  can be modeled as exponential
Plotted:
  SE under a constant model (slow and flat fading)
  SE under IID fading at each distance
See demo

## Slide 41: In-Class Exercise
Indoor environment
Look at large scale and small-scale fading

## Slide 42: Outline
Uncoded Modulation over Fading Channels
Capacity with Coding over Fading Channels: Outage Capacity
Capacity with Coding over Fading Channels: Ergodic Capacity
Review: Coding over an AWGN Channel
Coding over Fading Channels
Capacity with Bit-Interleaved Coded Modulation

## Slide 43: Coded Communication on an AWGN Channel
Channel coding
Symbol mapping
Channel with noise
Soft symbol demodulation
Channel decoder
Info bits
Coded bits
Info bits
LLR
We first review channel coding on a flat channel:
All details can be found in the digital communications class
TX symbols
RX symbols

## Slide 44: Uncoded vs. Coded Modulation
Uncoded Modulation:
  Modulate raw information bits
  One symbol at a time.
  Any symbol is in error, data packet is lost!
Coded modulation:
  Transmit in blocks (also called frames)
  Add extra parity bits to each block for reliability
  Decode entire block together
Info bits
Symbol mapping
Complex symbols
Info bits block
Coding
Info
Parity
Coded bit block
Block of symbols
Symbol mapping

## Slide 45: Key Parameters of Block Codes
An block code has:
  = number of information bits (input block size)
  = number of coded bits (output block size)
  = number of additional bits, typically parity
  = coding rate = .
Typical values in wireless:
  Block size: to 10000
  Code rate: to
k information bits
“message”
k info bits
n-k parity
“Bit Codeword” : n coded bits
Coding

## Slide 46: Coded Communication on an AWGN Channel
Channel coding
Symbol mapping
Channel with noise
Soft symbol demodulation
Channel decoder
Info bits
Coded bits
Info bits
We first review channel coding on a flat channel:
TX symbols
RX symbols

## Slide 47: Soft Symbol Demodulation
Set-up: Coded bits get mapped to symbol
  Receive
Uncoded systems use hard decision detection:
  Estimate bits from symbol
  Makes a discrete decision.
Coded systems generally use soft decision demodulation:
  Output log likelihood ratios:
  positive more likely
  negative more likely
Soft demod
Symbol mapping
+

## Slide 48: LLR for QPSK
TX symbol:
RX symbol:
LLR for bit
  [Each dim has
  Likelihood:
  With some algebra:
01
11
10
00
Mapping of bits

## Slide 49: QPSK LLR Visualized
LLR for is:
LLR for is:
Mapping of bits
more likely
more likely

## Slide 50: High Order Constellations
Higher order constellations (eg. 16- or 64-QAM)
Each constellation is a point is a function of multiple bits.
Example: For 16-QAM
  In phase dimension depends on bits
Cannot compute LLR on an individual bit directly
Two bits:
00
01
11
10
Mapping of bits

## Slide 51: High Order Constellations
To create LLRs for individual bits use total probability rule:
Resulting bitwise LLR:
Two bits:

## Slide 52: High Order Constellation Examples
2 bits / dim (16-QAM)
3 bits / dim (64-QAM)

## Slide 53: Approximate Bitwise LLR
Exact LLR:
  Can be too computationally expensive
Approximate LLR. For small:
  Typically, very close to exact LLR
  Computationally simpler. Avoid exponentials and logarithms

## Slide 54: Coded Communication on an AWGN Channel
Channel coding
Symbol mapping
Channel with noise
Soft symbol demodulation
Channel decoder
Info bits
Coded bits
Info bits
LLR
We first review channel coding on a flat channel:
TX symbols
RX symbols

## Slide 55: Maximum Likelihood Channel Decoding
Channel coding: Information block: generates a codeword
Receiver gets a vector number of complex modulation symbols
Channel decoder: Goal is to estimate (or equivalently ) from .
Ideally will use maximum likelihood decoding:
  Finds the codeword that is most likely given the receive vector
Channel coding
Symbol mapping
Channel with noise
Demod
Channel decoder
Info bits
Coded bits
Info bits
LLR
TX symbols
RX symbols

## Slide 56: Decoding from LLRs
LLRs sent to decoder:
Decoder typically approximates:
  The codeword most likely to produce the observed LLRs
  Works on LLRs not RX symbols
Channel coding
Symbol mapping
Demod
Channel decoder
Info bits
Coded bits
Info bits
LLRs
TX symbols
RX symbols

## Slide 57: Decoding from LLRs via Bitwise Approx
Bitwise independent approximation: Assume
  Ignore dependencies between coded bits
Under bitwise independent approximation, optimal decoder is:
  LLR for coded bit
  Proof in digital communications class
Demod
Channel decoder
Codeword
LLRs
RX symbols

## Slide 58: Decoding Complexity
Channel decoding ideally selects codeword
Brute force optimization is exponentially difficult:
  Suppose the information block is
  Each generates one codeword
  Optimization must, ideally, search over possible codewords
  Computationally impossible
Coding design requires searching over coding mechanisms with:
  Computationally tractable decoding
  But still have good performance

## Slide 59: Quest for the Shannon Limit
Shannon capacity formula and random codes, 1948.
  Determines the capacity, but no practical code to achieve it.
Hamming (7,4) code, 1950
Reed-Solomon codes based on polynomials over finite fields, 1960
  Used in Voyager program, 1977. CD players, 1982.
Convolutional codes.
  Viterbi algorithm, 1969. Widely used in cellular systems. (Viterbi later invents CDMA and founds Qualcomm)
  Typically, within 3-4 dB of capacity
Turbo codes, Berrou, Glavieux, Thitimajshima, 1993.
  Able to achieve capacity within a fraction of dB.
  Adopted as standard in all 4G and 5G cellular systems by the late 1990s.
LDPC codes
  Similar iterative technique as turbo codes. Re-discovered in 1996.
  Used in 5G systems
See digital communications class for many examples

## Slide 60: Convolutional Codes
Encode data through parallel binary (usu. FIR) filters
Example convolutional code:
  Rate = ½ (two output bits (for each input bit .
  Constraint length K=3 (size of shift register)
  Additions are modulo two
Benefits:
  Easy to implement, good performance
  Can be decoded with Viterbi algorithm Iterative procedure similar to dynamic programming procedure
  See digital comm class for more details
b[t]
c1[t]
c2[t]
z-1
z-1
z-1

## Slide 61: Convolutional Code Performance
Convolutional codes performance:
  > 5 dB better than uncoded BPSK at low BER
Only moderate constraint length (K=7) needed
Source: Proakis, “Digital communications”

## Slide 62: Simulation in MATLAB
MATLAB has excellent tools
  Conv encoder / decoder
  LLR
See demo
Rate=1/2, QPSK, K=7 conv code

## Slide 63: Turbo Codes
Turbo codes:
  Concatenation of two convolutional codes Typically IIR and short (K=3)
  Interleaver: Randomly permutes the input bits
Output
  Input bit, and
  Parity bits from each convolutional encoder
  With no puncturing R=1/3
Discovered in 1993, ,
  Berrou, Glavieux, Thitimajshima, 1993.
  Able to achieve capacity within a fraction of dB.
Used in 3G and 4G standards

## Slide 64: Turbo Code Iterative Decoding
Turbo decoder uses an iterative message passing
  Decode each convolutional coder one at a time
  Use posterior information of one code as prior for the other
Good performance in small number (usu. ~8) iterations
  Typically use short codes (K=3).
  Complexity similar to convolutional codes
Close to Shannon capacity
  Much better than convolution codes
Source: Lin, Costello, “Error Control Coding”

## Slide 65: LDPC Codes
Code defined by a bipartite graph
  Connects coded bits and parity bits
  Data information bits
Also use a message passing decoder
  Based on graphical models
Obtains excellent performance
  Lower complexity than turbo decoder
  Good for very high data rate applications
Used in 802.11ad and 5G New Radio
LDPC Graph
Coded bits
Parity check bits

## Slide 66: In-Class Problem
Simulate the commercial 5G NR LDPC code
  A rate 1/3 code
  Much better performance than convolutional code

## Slide 67: Outline
Uncoded Modulation over Fading Channels
Capacity with Coding over Fading Channels: Outage Capacity
Capacity with Coding over Fading Channels: Ergodic Capacity
Review: Coding over an AWGN Channel
Coding over Fading Channels
Capacity with Bit-Interleaved Coded Modulation

## Slide 68: Coded Communication on a Fading Channel
Fading channel
Info bits
Info bits
Now consider fading channel:
To handle fading we need to introduce a few new blocks
  Interleaving and de-interleaving
  Equalization
Inter-leaver
Symbol mapping
Channel encoder
Equal-ization
De-inter-leaver
Channel decoder
New blocks
New block

## Slide 69: Symbol Equalization via Inversion
Received noisy symbol:
Symbol equalization:
  Estimate from
  Also obtain a noise estimate (needed for LLR)
Channel inversion:
  Symbol estimate
  Noise estimate:
Symbol Equalization
+

## Slide 70: MMSE Symbol Equalization
Received noisy symbol:
MMSE estimation:
  Use linear estimate
  Select to minimize
Resulting estimate (shown with simple algebra):
  Estimate:
  Noise variance:
Provides lower noise estimate than channel inversion
Symbol Equalization
+

## Slide 71: Interleaving and De-Interleaving
Problem: Fading is correlated in time
  Will result in many consecutive faded bits
  Many codes perform poorly if errors are together
Interleaver
  Shuffles the bits before symbol mapping
  De-interleaving is performed on LLRs
  Randomizes locations of errors
  Removes time correlations
Many interleavers used in practice
  Random interleaver (with some seed at TX and RX)
  Row-column interleavers…
Inter-leaver
De-Interleaving

## Slide 72: Simulation
Simulation:
  Convolutional code, rate with QPSK
  Constraint length
  Plotted is block error rate (BLER) vs.
Gap between AWGN and fading:
  Approximately 3 dB at BLER =
  Much smaller gap than uncoded modulation

## Slide 73: Scaling the LLRs in MATLAB
Noise variance after equalization:
  Changes with channel gain
  Difference symbols have different
Recall that for approximate LLR:
MATLAB:
  Compute LLRs with noise variance = 1
  Then scale with noise variance
  Built-in scaling doesn’t appear to work
Manual noise scaling: Works
MATLAB built-in scaling: Does not work!

## Slide 74: Simulating in MATLAB
Transmitter and Channel Fading
Channel Noise and Receiver

## Slide 75: Summary
Fading: Causes variations in SNR
Uncoded modulation:
  Dramatically increases error rate
  Must add significant fade margin
Coding with flat and slow fading
  All symbols are faded together
  Fade margin still necessary
Coding with fast or frequency-selective fading
  Can greatly mitigate fading
  Recover faded bits with redundancy
  But needs to encoded over many independent fades
  Transmit over many coherence or bandwidth

## Slide 76: Outline
Uncoded Modulation over Fading Channels
Capacity with Coding over Fading Channels: Outage Capacity
Capacity with Coding over Fading Channels: Ergodic Capacity
Review: Coding over an AWGN Channel
Coding over Fading Channels
Capacity with Bit-Interleaved Coded Modulation

## Slide 77: Practical Fading Channel Capacity
Previously, we computed ergodic capacity
But achieving this capacity requires:
  Gaussian signaling while practical systems use M-QAM
  Ideal decoding while practical systems use bitwise LLRs
Bitwise Interleaved Coded Modulation
  An estimate of the capacity under constraints of using bitwise LLRs
Fading channel
Bitwise LLRs
Inter-leaver
Symbol mapping
Channel encoder
Equal-ization
De-inter-leaver
Channel decoder
Info bits
Coded bits

## Slide 78: Bitwise Channel
Fading channel
Inter-leaver
Symbol mapping
Channel encoder
Equal-ization
De-inter-leaver
Channel decoder
Info bits
Bitwise LLRs
Bitwise channel
Channel encoder
Channel decoder
Info bits
Coded bits
Noise and channel gain

## Slide 79: BICM Theorem
Bitwise LLRs
Bitwise channel
Channel encoder
Channel decoder
Coded bits
Noise and channel gain
Consider channel from coded bits to LLRs
  Theoretical capacity =
  Information bits / coded bit
Theorem: Mutual information is bounded below:
  Binary cross entropy:
Bound is exact when:
  for some received data
  are independent given

## Slide 80: BICM Capacity
Model
  QAM symbol
AWGN
Fading: i.i.d. complex Normal
Loss is ~2 dB with optimal MCS choice